## Slide 1
FootSense
smart insole tracker
A 10 crore rupee problem,
solved with a soldering iron
By: Arnav Gupta
Kinjal Mehta
Kiyansh Mahajan

## Slide 2
The Problem
9–18% of Indians show flat feet, depending on which clinical test you use
One study of traffic police in Gujarat found flat feet in 33–34% of officers — mostly from standing all day
24.8% prevalence found in a Delhi hospital screening study

## Slide 3
The Expensive Way
Clinical Gait Analysis System
FootSense
3D Gait Analysis System: ₹10,00,000+
FootSense: a few hundred rupees in sensors and a Sunday at Maker's Asylum

## Slide 4
What’s Actually in the Shoe
  3 flex sensors → arch shape (flat / normal / high)
  2 piezo discs → heel & forefoot impact
  MPU6050 → step count & impact angle
  ESP32 → WiFi → live dashboard
ESP32
MPU6050
flex sensor
piezo disc

## Slide 5
It Talks Back
Real Time Arch Bend
Step Count + Impact Angle
Foot Diagnosis
Impact Pressure (Graph and Data)
Live Dashboard

## Slide 7
The Truth
  Load cell + 4-sensor bridge: didn't work, never fully diagnosed why
  Switched to flex sensors + piezo discs/velostat instead
  Chased ghost GPIO pins across three different boards
  Eventually got a working ESP32 + WiFi + live dashboard pipeline

## Slide 8
  Pressure-sensitive sheet, not discrete sensors
  Resistance drops the harder you press — wired as a simple voltage divider
  Gives a continuous pressure map instead of fixed points
  Closer to what ₹10,00,000 clinical mats actually do
  Tradeoff: more finicky to calibrate consistently
  Built in parallel — not a replacement, a second real path
The Velostat Version

## Slide 9
The Truth Again
  This is a relative signal, not a medical diagnosis
  Tested on one person, on one foot.
Honest Limitations

## Slide 10
Testing the product and collecting data. Doing further extensive research and training a neural network to develop an AI/ML finished software. Connect with doctors, share the data and use their feedback.
Launch the product on a small scale, connect with shoe/footwear giants and look to expand the product’s functionality and make more iterations.
Q1 Development
Finalize innovative product design and successfully complete precise sensor calibration process. Design a finalised protected prototupe and apply for a license,
Q2 Testing
Q3 Awareness
Roadmap

## Slide 11
Lab-grade insight. Maker-grade budget. Blood. Sweat. Tears. A LOT of work. Even more help from mentors.
Questions?
FootSense

## Slide 12
People We Want to Thank
The amazing teammates we had here.
The ENTIRE Maker Team:
Dakshat Sir
Anool Sir
Vaibhav Sir
Miss Amber
Miss Sushmita
Sahil Sir
Miss Richa
Sankalp
Kinshuk
Sovam
Gunjan
All Our friends here, and Makers Asylum
Simran
Adishi
Shyam
Bhoomika
Arjun
Jastin / Kalki 01
Sebi
for watching and always supporting us